## Slide 1: Digital Annealer
Presenter: Cheng-Han Hsieh, Ting-Yi Wu
Team 11
https://github.com/r08943099/MSOCFall2020/tree/main/final_project

## Slide 2: Outline
Introduction
  Operating principle
  Application Example
  Evaluation Results
High level synthesis
Conclusion
Reference

## Slide 3: Introduction

## Slide 4: Introduction
A Digital Annealer (DA) is a dedicated architecture for high-speed solving of combinatorial optimization problems mapped to an Ising model.
  Fully coupled bit connectivity
  High coupling resolution
Uses Markov Chain Monte Carlo as a basic search mechanism
Accelerated by the hardware implementation of multiple speed-enhancement techniques
  Parallel search
  Escape from a local solution
  Replica exchange
Combinatorial optimization problem
  Ising model
    The Energy Function equal tp the QUBO form of problem

## Slide 5: Ising model
Statistical model representing the spin
Atomic spins in two states(+1 or -1)
  +1 : up
  -1 : down
Two procedures:
  Anneling:
    State transition that lowers the local energy by the interaction with adjacent spins
  Random flip:
    A stochastic state transition to help escape from local minima

## Slide 6: Operating steps
Two phases
  Trial phase
    state-variable change that meets an acceptance criterion is selected
  Update phase
    selected variable is flipped and relevant signals that depend on the variable are updated accordingly
Notes: 選擇滿足驗收標準的狀態變量更改

## Slide 7: Escape from a local solution
When the state is at a local minimum of the Ising energy function, the probability of moving to a new state is small.
  Slows convergence

## Slide 8: Replica exchange
Multiple replica run at different temperature with a criterion based on the Metropolis
Exchange transition probability
  n : replica index
  : reverse temperature
  : A set of states of replica n
  : Energy of replica n

## Slide 9: DA Operation Review
Given an problem: 4 city TSP
Convert to ising model
Assume this is initial state

## Slide 10: DA Operation Review (cont.)
Trial phase (Parallel)
16 spins need trial
………….
ADB
ADB
ADB
ADB
Candidates
Random choose and update phase
(if at local minimum add Eoff)

## Slide 11: DA Operation Review (cont.)
Replica exchange
  Above operations will parallel run with different temperature
  After one update, exchanging replica with probability

## Slide 12: Application Example: TSP

## Slide 13: TSP
n-cities are modeled by a lattice-like graph that uses n2
  City number
  Visit order
The objective function is formulated as the summation of the distances along the route and the number of constraint violations.

## Slide 14: TSP(cont.)
A n-vertices TSP is formulated as:
  aik : vertex k is (is not) visited as the i-th city when aik = 1(0)
  Wkl : the weight (or distance) between vertices k and l
  Possible routes is (n - 1)! / 2
    Difﬁcult to obtain its optimal solution by brute force methods as n becomes larger.

## Slide 15: Mapping
Consider the energy function of the quadratic, unconstrained binary optimization (QUBO) format [16], the TSP is expressed by:
aik is converted to Ising model spin σik ∈{-1,+1}
The ﬁrst, second, and third terms of Eq. (5) are represented as follows, respectively.
objective function penalty(visit several at the same time)
penalty(visit vertex i twice or more )

## Slide 16: Issues discussion
The graph becomes quadratically large
Solutions fail to satisfy the constraints with quality
If the constraint term is emphasized, the solution quality will signiﬁcantly deteriorate
Naïve Ising model solvers are used, the probability of obtaining an optimal solution is very low for TSPs of any useful size.

## Slide 17: Evaluation Results (TSP LIB)

## Slide 18: HLS

## Slide 19: Hardware target overview
For each iteration:
Replica 1
Replica 2
Replica N
Replica exchange
Update best

## Slide 20: Fail to parallel in previous work
Replica : 20
Iteration : 10
0.149 x 20x10

## Slide 21: Fail to parallel in previous work(cont.)
Fail to improve 20X
Just 10X

## Slide 22: Replica exchange scheme
In replica exchange scheme, we can parallel execute with different temperature settings.
Since the Data structure in Baseline, it cannot implement the parallel scheme
What we imagine
Parallel
Actually
Sequential
replica1
replica2
replica3
replica1
replica2
replica3

## Slide 23: The Data structure bottleneck
All operation will through structure DA to do the operation
For each replica, they will copy qubit matrix to da.qubit_matrix
Each function rely on da.qubit_matrix to opreate
  Cause cannot do parallel

## Slide 24: Rebuild the Data Structure
Delete the DA structure
Each function rely on replica.qubit_matrix to operate
Possible to do parallel

## Slide 25: Baseline
Force all execute_replica() be individual
Copy this function to N copies
Will do parallel?
So inconvenience…

## Slide 26: Success to parallel replica scheme
Replica : 20, Iteration : 20
Parallel
0.198*20

## Slide 27: Success to parallel replica scheme(cont.)
Solution: Make sure each replica has a copy from some constant value
  E.g. Distance Matrix, parameter
  Cons: More hardware
    Parallel all replicas
Some Common
Datum should have N copies

## Slide 28: #pragma HLS allocation
By default, HLS tries to save resources by using the function multiple times
Same performance with good coding format

## Slide 29: #pragma HLS pipeline rewind
Use pipeline for each iteration
Latency improves, but source over usage

## Slide 30: Other prama
In the design, it needs to use many matrices to operate
  Array partition
In the replica exchange scheme, we use the same function simultaneously. But in the HLS tool, it consider there are same instance.
  Function Inline with template

## Slide 31: Pseudo random generator
The function finish by LFSR
Declare the seed

## Slide 32: Cosim Error message solved
Error:
Just need to adjust the script file
  Before : cosim_design
  After :cosim_design -trace_level all -tool xsim

## Slide 33: Cosim Result

## Slide 34: Conclusion

## Slide 35: Conclusion
We implement digital annealer into synthesizable C code.
Perform HLS on the design and improve the latency
Achieve full parallel by HLS

## Slide 36: The end and Q&A