## Slide 1: MSoC Final Project Report Key-enabled Secure Access and Execution Environment for Vehicles (KSAE)
Team 16
R08943112 王佐育
R08943169 葛顯峯
R08943171 石文緯
GitHub: https://github.com/Wen-Wei0914/2020_MSOC_FINAL

## Slide 2: Outline
Introduction to keyless entry systems
  Security concerns of keyless entry systems
Why using high level synthesis (HLS)
Introduction of Key-enabled Secure Access and Execution Environment for Vehicles (KSAE)
HLS optimizations
Security analysis of KSAE
Conclusion

## Slide 3: Introduction to Keyless Entry System

## Slide 4: Introduction to Keyless Entry System
Carry the Key Fob
v
Unlock the Vehicle
Lock the Vehicle
The user carries the key fob and approaches the vehicle.
When the user/key fob is within certain range to the vehicle, the doors automatically unlock themselves.
The doors lock themselves again on the leaving of the user/key fob.
v
v
Icon source: https://thenounproject.com/

## Slide 5: Security Concerns of Keyless Entry Systems
News source: https://www.zdnet.com/article/tesla-model-x-hacked-and-stolen-in-minutes-using-new-key-fob-hack/
Notes: https://www.zdnet.com/article/tesla-model-x-hacked-and-stolen-in-minutes-using-new-key-fob-hack/

## Slide 6: Why Using High-Level Synthesis

## Slide 7: Why Using High-Level Synthesis
Advanced cryptography algorithms are mostly implemented in the form of software, HLS provides a quick and neat design methodology for converting such algorithms into hardware implementation
Frequent changes in the design of secure architecture for embedded systems are time-consuming yet desperately needed, HLS design flow reduces a marvelous amount of time whenever the architecture requires a modification
HLS also provides a rather simple approach for the integration between different algorithms at the early age of design flow, making changing design according to specification modification much feasible and effortless

## Slide 8: Introduction of Key-enabled Secure Access and Execution Environment for Vehicles (KSAE)

## Slide 9: Block Design of the System

## Slide 10: State Transition Diagram of KSAE
Sleep Mode
Waiting for
Command
Idle
Build & Send
Response
Motion Sensor Triggered
No Trigger within 1 min
Challenge
Idle for 0.5 sec
Read & Send
Digest
Request
Digest
Sleep Mode
  Not accepting any challenge while running in low power mode
Waiting for Command
  The key fob waits for the challenge from the vehicle
Read & Send Digest
  The key fob reads the received command and sends back digest accordingly
Build & Send Response
  The key fob builds and sends the corresponding response back to the vehicle
Idle
  Idle for a short period of time according to current condition

## Slide 11: Operation Scenario of KSAE
Icon resource: https://thenounproject.com/
Sleep Mode
Waiting for
Challenge
Motion Sensor Triggered
Door handle Triggered
Sleep Mode
Build
Challenge
(Asymmetric)
Send
Challenge
Build
Response
(Asymmetric)
Send
Response
Door Unlock
Secure Execution
Verify
Response
(Asymmetric)
Secure Execution
Verification
passed

## Slide 12: Operation Scenario of KSAE
Build
Response
(Symmetric)
Verify
Response
(Symmetric)
Verification
passed
Send
Challenge
Send
Response
Secure Execution
Read
DigMotor
Request
DigMotor
Match?
Motor
on
Integrity
Verification
(Motor
Control
Program)
Calculate
DigMotor
Return
DigMotor
*DigMotor: HMAC (Keyed-hash message authentication code) Digest of Motor Control Program
Open
Door
&
Build
Challenge
(Symmetric)
Verification
passed

## Slide 13: HLS Optimization of KSAE

## Slide 14: HLS Optimization of KSAE
Source: https://en.wikipedia.org/wiki/Block_cipher_mode_of_operation

## Slide 15: HLS Optimization of KSAE
Example 1. SHA-256 (Secure Hash Algorithm)
-> approx. 26% time reduction

## Slide 16: HLS Optimization of KSAE
Example 2. ECC (Elliptic Curve Cryptography) encryption

## Slide 17: HLS Optimization of KSAE
Overall timing improvement
-> approx. 27% time reduction

## Slide 18: Security Analysis of KSAE

## Slide 19: Common Attacks for Keyless Entry Systems
Scan attack:
Scans for information stored on embedded systems
Replay attack:
Replays previous valid response for trespassing verification
Challenge forward prediction attack:
Observes sent challenges and predicts possible challenges
Dictionary attack:
Stores challenge-response pairs and responds accordingly
Relay attack:
Intercepts transmission between devices and tricks the receiver
with intercepted signal

## Slide 20: Security Analysis
Claim 1.
The proposed KSAE prevents challenge forward prediction attack.
Proof.
  The challenges in our protocol is generated through PUF, whose randomness passes the Cryptographic Validation Program (CAVP) of National Institute of Standards and Technology (NIST).
  The challenges are therefore unpredictable and the seed value is renewed whenever the system enters sleep mode.

## Slide 21: Security Analysis
Claim 2.
The proposed KSAE raises the difficulty of scan attack.
Proof.
The KSAE idles for 0.5 seconds whenever a faulty response is received, making the scan attack a rather time-consuming process which greatly raises the computing time of scan attack, disregard of computing capacity of the attacker’s equipment.

## Slide 22: Security Analysis
Claim 3.
The secret keys are not revealed to the attackers.
Proof.
The secret keys used during the operation is stored within the Zynq-7000 SoC of ZedBoard and not transferred outside of the chip, making it impossible to probe the secret unless by de-capping the chip, which will possibly sabotage the chip

## Slide 23: Conclusion
HLS tremendously reduces the design time for secure embedded systems
HLS also provides a quick and neat design flow for systems that require frequent change in architecture during design
Several different solutions are tried and an qualified final version was built with the time reduction of 27%

## Slide 24: Thank You

## Slide 25: Appendix

## Slide 26: Appendix A.1 Public Key Certificate Verification

## Slide 27: Appendix A.2 Key Fob Asymmetric Authentication
*privKeyKF: Private Key of Key Fob
*pubKeyKF: Public Key of Key Fob
*TRNG: True Random Number Generator
*SHA(C): SHA-256(Challenge)
*SigKF: Digital Signature of ECDSA_Sign
*RNKF: Random Number generated by
Key Fob

## Slide 28: Appendix B.1 Key Fob Asymmetric Authentication
*TRNG: True Random Number Generator
*SNKF: Serial Number of Key Fob
*pufKey: SRAM PUF Key
*deKeyKF: Derived Key of Key Fob

## Slide 29: Appendix B.2 Software Integrity Verification
*ProgMotor: Motor Control Program
*DigMotor: HMAC Digest of ProgMotor